## Slide 1: Eels in the River Leadon measures, models & management plans
Alan Walker: alan.walker@cefas.co.uk
Jon Hateley: jon.hateley@environment-agency.gov.uk
Background
EU Regulation => Eel Management Plans => silver eel escapement per RBD (11)
Problem = few silver eel fisheries
Solution 1 = scientific counters
BUT – few fixed sites & v. expensive to operate
Solution 2 = lots of yellow eels surveys, so ....
extrapolate yellow to silver using model
BUT – model requires validation

## Slide 2
R. Leadon
tributary of the Severn
Counting Silver eels
DIDSON acoustic camera
Sargasso
Area 106 ha
Length 43 km
DIDSON: Multibeam sonar with fish counting capabilities in turbid waters.
Eels counted and lengthed.
Raw downstream biomass estimates corrected for system downtime, motion detection efficiency and unsampled water.

## Slide 3
INPUTS
13 reaches = length, area
Yellow eel surveys = density, length freq’y
MODELLED PROCESSES
Growth, differentiation, natural mortality,
dispersal, silvering; & density influences
OUTPUTS
Annual time series:
Reach-specific yellow eel density & biomass (U, M, F)
& length frequency distributions
Silver eel escapement numbers & biomass (M, F)
& length frequency distributions
Comparisons (kg/ha)
Estimator | 2009 | 2010
DIDSON | 0.94 | 0.48
SMEP II | 1.42 | 1.34
Life-history model
Scenario-based Model Eel Population (SMEP II)