## Slide 1: ORCA (Antarctic cosmic ray observatory): 2018 Latitudinal Survey, preliminary results
Anna Morozova1, J. J. Blanco2, Ó. García Población2, C. T. Steigies3, J. I. García Tejedor2, J. Medina2, M. Prieto2, A. López-Comazzi2, S. Ayuso2, R. Gómez-Herrero2, J. A. Garzón4, D. García-Castro4, P. Cabanelas4, A. Gomis-Moreno5, V. Villasante-Marcos5, B. Heber3, G. Kornakov6, T. Kurtukian7, A. Blanco8, L. Lopes8, J.P. Saravia8, H. Kruger9, Du Toit Strauss9
1 CITEUC, University of Coimbra, Portugal, 2 University of Alcalá, Spain.; 3 IEAP, Christian Albrechts Universität zu Kiel, Germany; 4 University of Santiago de Compostela, Spain; 5 Instituto Geográfico Nacional, Madrid, Spain; 6 TU-Darmstadt, Germany; 7 CENBG, IN2P3/CNRS-Université Bordeaux, France; 8 LIP-Coimbra, Portugal; 9 Center for Space Research , North-West University, South Africa
EGU2019-10894

## Slide 2: ORCA & TRISTAN co-operation

## Slide 3: Cosmic ray latitudinal survey
MITO, NEMO & TRISTAN have performed a latitudinal observation from Vigo (Spain) to Juan Carlos I Spanish Antarctic Base (Livingston Island, Antarctic Peninsula) aboard the Sarmiento de Gamboa oceanographic vessel from 14 November, 2018 to 2 January, 2019.
The latitudinal survey took ORCA throughout the South Atlantic Magnetic Anomaly along the Brazilian coast.

## Slide 4: ORCA: NEMO & MITO
ORCA is integrated by a set of detectors able to measure fluxes of neutrons, charged particles (mostly muons) and muons incident directions on the detector surface. The combination of these detectors allow us to measure neutrons, muons, protons, electrons and gamma rays arriving to ORCA’s location
MITO (top)
ORCB
ORCA
MITO (bottom)
NEMO

## Slide 5: NEMO
ORCA instrument consists of two neutron monitors:
  ORC-B (top, without lead): 3 bare BF3 counters
  ORC-A (bottom, with lead): 3 BF3-based 3NM64
Count rate (6 channels): 1 min data
ORC-B
ORC-A

## Slide 6: MITO
MITO instrument consists of a muon telescope:
  2 BC-400 scintillators
    size: 100 x 100 x 5 cm
    with lead between the top & bottom plates
  2 x 4 PMTs gathering light from the lateral faces
Count rate (1 min data):
  Top & bottom plates
Coincidence 8 PMTs
TBA:
  muon energy
  incoming direction
MITO

## Slide 7: TRISTAN
TRISTAN is a multitrack detector with μ/e separation
3 timing-RPC planes
  size: 1.50 x 1.20 m2
  90 read-out channels
Performances
    σX = σY ~ 6.5cm
    σΩ = 0.1 sr
    σT = 0.3 ns
    σV = 20% c
Coincidence trigger: T1*T3
Particle identification: μ, γ, e, p

## Slide 8: From Spain to Antarctic

## Slide 9: From Spain to Antarctic

## Slide 10: @ JCI-BAE

## Slide 11: Cut-off Rigidity VS Time
1
2
SAA
4
5
3
4
5
0
0
1
2
3
SAA
4
5

## Slide 12: Data
Raw data (no correction for p, T, cut-off R...)
1 min original time resolution for NEMO & MITO
10 min original time resolution for TRISTAN
3σ outliers removed
Smoothed: 1 h running mean

## Slide 13: Cosmic ray VS Time
NEMO
TRISTAN
MITO
ORCA
ORCB x 5
Bottom
Top Coin8 x 50
NEMO
ratio ORCA/ORCB

## Slide 14: Cosmic ray VS Cut-off Rigidity
NEMO
MITO
NEMO
ORCA
ORCB x 5
Bottom
Top Coin8 x 50
ratio ORCA/ORCB
TRISTAN

## Slide 15: Environment VS Time

## Slide 16: Cosmic ray VS Environment
NEMO
MITO
ORCA
ORCB x 5
Bottom
Coin8 x 50 Top

## Slide 17: Now...
  ORCA/B & MITO stay alone in Antarctic
    @ JCI-BAE from 20 January, 2019 to present
    stops to work on 30 March (no sun?). We have to wait until the batteries are recharging
  TRISTAN
    on its way back measuring CR
    expected @ Vigo ~April 9

## Slide 18: Questions?