## Slide 1: Robustness Metrics
How are they calculated and when should they be used?
C. McPhail, H.R. Maier, J.H. Kwakkel, M. Giuliani, A. Castelletti and S. Westra

## Slide 2: How do we plan for an uncertain future?
Notes: Environmental decision-making has long required planning for an uncertain future
An example is a water supply system: large-scale infrastructure, large costs, long planning period (decades)

## Slide 3: How do we plan for an uncertain future?
Estimated distribution of future states
(Scenario #1)
Estimated distribution of future states
(Scenario #2)
System state
Today
Future
Notes: DMs are increasingly considering multiple plausible futures (scenarios) to represent futures where the relative likelihoods are unknown
(example could be RCP4.5 and RPC8.5)

## Slide 4: How do we quantify system performance under uncertainty?
System performance
System performance
System state
Today
Future
Relative likelihood of occurrence is unknown
Notes: For each of the projected futures (scenarios) we can calculate the system performance as per before (e.g. reliability)
But we don’t know the likelihood of each of these futures

## Slide 5: How do we quantify system performance under uncertainty?
System performance
System performance
Robustness
System state
Today
Future
Relative likelihood of occurrence is unknown
Notes: So we consider the concept of robustness: the greatest performance, across as many futures as possible

## Slide 6: Which metric should we use for calculating robustness?
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion
Notes: The literature for robustness is full of these different metrics
But they are all reflecting different aspects of what it means to have the greatest performance over as many scenarios as possible
Some focus on maximising performance for some scenarios
Others focus on having consistent performance across as many scenarios as possible
So it’s difficult for DMs to know which one to use, because they are all telling you different things

## Slide 7: Which metric should we use for calculating robustness?
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion
Notes: One of the oldest metrics is the Maximin metric
Wald, 1950
Economics
Looking at maximising the worst-case performance

## Slide 8: Which metric should we use for calculating robustness?
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion
Notes: Starr, 1963

## Slide 9: Which metric should we use for calculating robustness?
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion
Notes: Kwakkel, 2016

## Slide 10: Contributions of the research
A unified framework for the calculation of a wide range of robustness metrics. Enabling a comparison of robustness metrics.
A taxonomy of robustness metrics. Providing guidance to decision-makers.

## Slide 11
Plausible future conditions (Scenarios)
Decision alternatives (e.g. Policy options, plans, solutions)
Performance metric (e.g. cost, reliability)
Robustness value
Robustness metric
Notes: To begin the unifying framework, need to look at what all metrics have in common
They all take the decision alternatives, …, …, and they filter this through the robustness metric to produce the robustness value

## Slide 12
Chart: Transformed Performance
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.95 | 0.83 | 0 | 0.9
 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85
Chart: Scenario #
| 1 | 2 | 4 | …
Performance | 0.02 | 0.05 | 0.02 | 0
Performance over all scenarios
Transformed performance values over all scenarios
Transformed performance values over selected scenarios
Robustness value
Mean
T1: Performance value transformation
T2: Scenario subset selection
T3: Robustness metric calculation
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
Performance | 0.02 | 0.05 | -0.1 | 0.02 | 0 | -0.05
Notes: The unifying framework allows the categorisation of the metrics according to 3 transformations, T1, T2, T3
All of the metrics use these transformations to get from the performance in each scenario, to the value of robustness
We start with all of the performance values and apply the performance value transformation
From these transformed values, we select a subset of scenarios
From the subset, we calculate some value based on the distribution of performance values, and this gives us the robustness

## Slide 13: T1: Performance value transformation
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
Performance | 0.02 | 0.05 | -0.1 | 0.02 | 0 | -0.05
Performance (identity)
Cost of making wrong decision (regret)
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.95 | 0.83 | 0 | 0.9
 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.02 | 0.02 | 1 | 0.02 | 1
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.95 | 0.83 | 0 | 0.9
Performance values
Pass/fail (satisficing)
OR
OR
Threshold
Notes: The performance values are transformed depending on the needs of the DM
If there is an important threshold (e.g. supply > demand, see dotted line) then it may make sense to use a satisficing metric, where we only care about whether the decision alternative passes or fails.
Otherwise you might be most interested in minimising the regret (cost of making the wrong choice). E.g. in a water supply system you want to minimise unnecessary overexpenditure
You might just want to maximise the performance itself, in which case the Identity transform is fine. E.g. if you’re looking at a stream restoration with a fixed budget, it might be best to just consider maximising performance

## Slide 14: T1: Performance value transformation
 | Robustness calculation based on relative performance values | Robustness calculation based on absolute performance values
Indication of whether system performance is satisfactory or not | (MORE) (POMORE) (Decision Scaling) | Starr’s domain criterion (Info Gap)
Indication of actual system performance | Minimax regret 90th percentile minimax regret Undesirable deviations | Maximin (minimax) Maximax Hurwicz’s optimism-pessimism rule Laplace’s principle of insufficient reason Mean-variance Percentile-based skewness Percentile-based peakedness

## Slide 15: T2: Scenario subset selection
Worst half of scenarios
Best-case scenario
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.95 | 0.83 | 0 | 0.9
Transformed performance values
Worst-case scenario
OR
OR
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.8 | 0
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.95
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.83 | 0
Notes: Second transformation is the scenario subset selection
This is asking which performance values should be used? The worst-case? The best-case?
Some subset?
Or all values?

## Slide 16: T2: Scenario subset selection
Less risk averse
More risk averse
Notes: This transformation is related to the level of risk aversion that the DM has
At the bottom you have the maximin metric which represents a very risk averse metric, assuming that the worst-case scenario will happen
  This might be most relevant when considering the design of a dam, where failure could kill 1000s of residents
At the top you have the maximax metric which represents a lower level of risk aversion
  This might be more relevant for something such as the design of a stormwater system, which will be unlikely to kill 1000s of people

## Slide 17: T3: Robustness metric calculation
Chart: Transformed Performance
Skew
Variance
Transformed performance values in selected scenarios
Expected value
(e.g. mean)
OR
OR
Mean
Chart: Transformed Performance
Chart: Transformed Performance
Variance
Chart: Transformed Performance
Mean
Median
Notes: We have a distribution of transformed performance values in the selected scenarios
Generally DMs are interested in the expected value. E.g. cost or reliability. And therefore use the sum or mean of the performance values
For supplemental info, a DM might use variance or some higher-order statistic from the distribution to understand the difference between decision alternatives with similar expected value:
  Variance – spread of performance
  Skew – difference in performance under extreme conditions
  Kurtosis – consistency in performance

## Slide 18: T3: Robustness metric calculation
Robustness metric | Robustness metric calculation |  |  |  |  |  | 
 | None | Sum | Mean | Weighted mean | Variance | Skew | Kurtosis
Maximin | ✓ |  |  |  |  |  | 
Maximax | ✓ |  |  |  |  |  | 
Hurwicz optimism-pessimism rule |  |  |  | ✓ |  |  | 
Laplace’s principle of insufficient reason |  |  | ✓ |  |  |  | 
Minimax regret | ✓ |  |  |  |  |  | 
90th percentile minimax regret | ✓ |  |  |  |  |  | 
Mean-variance |  |  | ✓ |  | ✓ |  | 
Undesirable deviations |  | ✓ |  |  |  |  | 
Percentile-based skewness |  |  |  |  |  | ✓ | 
Percentile-based peakedness |  |  |  |  |  |  | ✓
Starr’s domain criterion |  |  | ✓ |  |  |  | 

## Slide 19
Chart: Transformed Performance
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
 | 0.83 | 0.8 | 0.95 | 0.83 | 0 | 0.9
 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85
Chart: Scenario #
| 1 | 2 | 4 | …
Performance | 0.02 | 0.05 | 0.02 | 0
Performance over all scenarios
Transformed performance values over all scenarios
Transformed performance values over selected scenarios
Robustness value
Mean
T1: Performance value transformation
T2: Scenario subset selection
T3: Robustness metric calculation
Chart: Scenario #
| 1 | 2 | 3 | 4 | … | n
Performance | 0.02 | 0.05 | -0.1 | 0.02 | 0 | -0.05
Notes: We’ve developed this unifying framework with three transformations
T1: Is there some important threshold such as supply > demand? Are you interested in minimising the cost of making a wrong decision? Are you interested just in maximising performance?
T2: How risk averse do you need to be for this problem? This effects the scenarios that are selected.
T3: Are you interested in the expected value of performance? Or are you interested in looking at how the performance varies across scenarios?

## Slide 20
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion

## Slide 21
Metric | T1: Performance value transformation | T2: Scenario subset selection | T3: Robustness metric calculation
Maximin | Identity | Worst-case | Identity
Maximax | Identity | Best-case | Identity
Hurwicz optimism-pessimism rule | Identity | Worst- and best-cases | Weighted mean
Laplace’s principle of insufficient reason | Identity | All | Mean
Minimax regret | Regret from best decision alternative | Worst-case | Identity
90th percentile minimax regret | Regret from best decision alternative | 90th percentile | Identity
Mean-variance | Identity | All | Mean-variance
Undesirable deviations | Regret from median performance | Worst-half | Sum
Percentile-based skewness | Identity | 10th, 50th and 90th percentiles | Skew
Percentile-based peakedness | Identity | 10th, 25th, 75th and 90th percentiles | Kurtosis
Starr’s domain criterion | Satisfaction of constraints | All | Mean
Maximin
Maximax
Hurwicz optimism-pessimism rule
Laplace’s principle of insufficient reason
Minimax regret
90th percentile minimax regret
Mean-variance
Undesirable deviations
Percentile-based skewness
Percentile-based peakedness
Starr’s domain criterion

## Slide 22
Metric | T1: Performance value transformation | T2: Scenario subset selection | T3: Robustness metric calculation
Maximin | Identity | Worst-case | Identity
Maximax | Identity | Best-case | Identity
Hurwicz optimism-pessimism rule | Identity | Worst- and best-cases | Weighted mean
Laplace’s principle of insufficient reason | Identity | All | Mean
Minimax regret | Regret from best decision alternative | Worst-case | Identity
90th percentile minimax regret | Regret from best decision alternative | 90th percentile | Identity
Mean-variance | Identity | All | Mean-variance
Undesirable deviations | Regret from median performance | Worst-half | Sum
Percentile-based skewness | Identity | 10th, 50th and 90th percentiles | Skew
Percentile-based peakedness | Identity | 10th, 25th, 75th and 90th percentiles | Kurtosis
Starr’s domain criterion | Satisfaction of constraints | All | Mean

## Slide 23: Future work
A conceptual framework for understanding when robustness metrics agree or disagree.
Paper under revision
C. McPhail, H.R. Maier, J.H. Kwakkel, M. Giuliani, A. Castelletti and S. Westra (under revision), Robustness metrics: How are they calculated, when should they be used and why do they give different results?, Earth’s Future.
Contact
Cameron McPhail University of Adelaide cameron.mcphail@adelaide.edu.au

## Slide 24: T1: Performance value transformation
Description | Equation
Identity transformation | 
Regret from best decision alternative | 
Regret from median | where is the median performance for decision alternative . i.e.
Satisfaction of constraints | where is a constraint
Description | Equation
Identity transformation | 
Regret from best decision alternative | 
Regret from median | 
Satisfaction of constraints | 

## Slide 25: T2: Scenario subset selection
Description | Equation
Worst-case | 
Best-case | 
Worst- and best-cases | 
All | 
Worst-half | where is the 50th percentile (median) value of
Percentile | where is the kth percentile value of Note that the scenario that produces the value of closest to is the scenario that is used.
Description | Equation
Worst-case | 
Best-case | 
Worst- and best-cases | 
All | 
Worst-half | 
Percentile | 

## Slide 26: T3: Robustness metric calculation
Description | Equation
Identity transformation | 
Mean | where is the number of scenarios in
Sum | 
Weighted mean (two scenarios) | where and are two scenarios and is the preference of the decision maker towards using and
Description | Equation
Identity transformation | 
Mean | 
Sum | 
Weighted mean (two scenarios) | 
(Also see next slide…)

## Slide 27: T3: Robustness metric calculation
Description | Equation
Variance-based (i.e. the standard deviation) | where is the mean (see the equation earlier in this table)
Mean-variance | where is the mean and is the standard deviation (given by equations above)
Skew | where , and are scenarios that represent the 10th, 50th and 90th percentiles for
Kurtosis | where , , and are scenarios that represent the 10th, 25th, 75th and 90th percentiles for
Description | Equation
Variance-based (i.e. the standard deviation) | 
Mean-variance | 
Skew | 
Kurtosis |