## Slide 1: Probabilistic flood mapping: Stochastic Galerkin shallow water model with uncertain source terms
James Shaw & Georges Kesserwani (University of Sheffield)
Per Pettersson (Norwegian Research Centre)

## Slide 2: About me
2002–2005 BSc Computer Science
University of Southampton
2005–2013 Software engineer
2013–2018 MSc and PhD Atmosphere Ocean & Climate
University of Reading
  High-order FVM on arbitrary unstructured meshes
  Vertical coordinates for well-balanced flows over mountains
April 2018– University of Sheffield
  Multiwavelet-based adaptive DG methods
  Stochastic Galerkin methods for probabilistic flood mapping

## Slide 3: Smart flood forecasting infrastructure with uncertainties
Resolution
Technique
Accuracy
Robust flood model
1000+ iterations
Uncertainty
quantification
Multiwavelet-based
adaptivity
2nd-order DG
Automated meshing
Minimal configuration

## Slide 4
Measurement errors
Terrain and river bed elevation
River water levels and flow rates
Extrapolation errors
River flow rate often extrapolated from water level
Simulating 1-in-100 year event with only ~30–40 years of observations
Parameter errors
Friction parameter is calibrated against observations to account for sub-grid scale processes and numerical errors
Uncertainties in flood modelling

## Slide 5
Simulation of a 1-in-100 year flood event
20000 Monte Carlo samples
Simulation took 3 days with compute cluster of 100 desktops
Current state-of-the-art
probabilistic flood mapping
Source: Neal et al. 2013 doi.org/c3jj

## Slide 6: Can we do better using a stochastic Galerkin approach?
We seek a stochastic Galerkin model that:
is substantially more efficient than Monte Carlo
produces sufficiently accurate probability distributions
preserves robust properties of deterministic model

## Slide 7
Well-balancing: water remains motionless
Robust properties of deterministic models

## Slide 8
Well-balancing: water remains motionless
Dynamic wetting-and-drying (water depth ≥ 0)
Source: hydrologyexpert.com
Robust properties of deterministic models

## Slide 9
Well-balancing: water remains motionless
Dynamic wetting-and-drying
Shock-capturing, ability to model subcritical and supercritical flow transitions
Source: doi.org/c3jh
Robust properties of
deterministic models

## Slide 10
Well-balancing: water remains motionless
Dynamic wetting-and-drying
Shock-capturing, ability to model subcritical and supercritical flow transitions
Decades of research into making deterministic models robust
Stochastic Galerkin models do not automatically inherit robustness properties
Robust properties of deterministic models

## Slide 11
Develop a 1D stochastic Galerkin model with:
  Single stochastic dimension to represent uncertain terrain
  Robust well-balancing over highly irregular and uncertain terrain
  Fully wet, frictionless domain
Extend the 1D model to include:
  Multiple stochastic dimensions
  Uncertain friction parameter
  Dynamic wetting-and-drying
Assess model robustness, accuracy and sensitivity to the stochastic approximation
Aims

## Slide 12: Well-balanced stochastic Galerkin model For fully-wet, frictionless domains

## Slide 13: Deterministic 1D shallow water equations with terrain source term
z(x) terrain elevation
h(x, t) water depth
u(x, t) depth-average horizontal velocity
q(x, t) discharge (mass flux)
η(x, t) free-surface elevation

## Slide 14: Deterministic 1D shallow water equations with terrain source term
Flow vector
Flux vector
Water depth
Unit-width discharge
Source term vector
Terrain profile

## Slide 15: Finite volume Godunov-type discretisation

## Slide 16: Finite volume Godunov-type discretisation
Fixed timestep
Uniform mesh spacing
Numerical fluxes
Shock-capturing Roe approximate Riemann solver
Surface gradient method ensures discrete balance between of numerical flux and terrain gradients

## Slide 17: Surface gradient (interface) method
Calculate modified topography data that enforces continuity at interfaces

## Slide 18: Surface gradient (interface) method
Calculate modified topography data that enforces continuity at interfaces
Calculate modified water depth and discharge data based on:
  original free-surface elevation
  original flow velocity
  modified topography data
(K is + or −)

## Slide 19: Surface gradient (interface) method
Calculate modified topography data that enforces continuity at interfaces
Calculate modified water depth and discharge data based on:
  original free-surface elevation
  original flow velocity
  modified topography data
Use modified variables to calculate Riemann fluxes and source term
(K is + or −)

## Slide 20: Stochastic Galerkin reformulation
Turn deterministic variables into stochastic variables
Rewrite the deterministic discretisation using these stochastic variables
Make a stochastic Galerkin projection onto the basis functions

## Slide 21: 1. Deterministic variables become stochastic variables
Each stochastic variable is approximated by an orthogonal basis expansion
Orthogonal basis functions Φp
Expansion
coefficients
  Stochastic coordinate ξ
  Basis order P

## Slide 22: 1. Deterministic variables become stochastic variables
Each stochastic variable is approximated by an orthogonal basis expansion
Every water depth, discharge and terrain variable become stochastic variables

## Slide 23: 2. Rewrite discretisation using stochastic variables
Deterministic:

## Slide 24: 2. Rewrite discretisation using stochastic variables
Stochastic:

## Slide 25: 2. Rewrite discretisation using stochastic variables
where
Stochastic:

## Slide 26: 3. Stochastic Galerkin projection
Need to decouple this equation to solve for each

## Slide 27: 3. Stochastic Galerkin projection
Since the basis functions are orthogonal then
and
for any stochastic variable X(ξ)
Need to decouple this equation to solve for each

## Slide 28: 3. Stochastic Galerkin projection
we can decouple the equations and solve for each
Using the orthogonality property

## Slide 29: 3. Stochastic Galerkin projection
we can decouple the equations and solve for each
Using the orthogonality property

## Slide 30: 3. Stochastic Galerkin projection
Using the orthogonality property
we can decouple the equations and solve for each
Nonlinear functions
Constants
precalculated exactly
Quadratic function

## Slide 31: 3. Stochastic Galerkin projection
Quadrature weights
Quadrature points
Quadrature approximation of the flux:
Use of quadrature makes this a pseudo-intrusive method as opposed to a fully-intrusive method
(Tryoen et al. 2010, doi.org/dpsnv4)

## Slide 32: 3. Stochastic Galerkin projection
Quadrature weights
Quadrature points
Source term vector approximated with a pseudo-spectral product:
Constants precalculated exactly
Quadrature approximation of the flux:

## Slide 33: Numerical results using classical Wiener–Hermite basis

## Slide 34: Lake-at-rest over uncertain terrain
Used to verify the well-balanced property.
We will compare:
Centred difference model
  Centred difference approximation of terrain source term
  Not well-balanced
Well-balanced model
  Surface gradient method
  Expected to be well-balanced

## Slide 35: Lake-at-rest uncertain terrain profile
± 1 stddev

## Slide 36: Lake-at-rest solutions after 100s (~670 timesteps)
Δx = 1 m
Basis order P = 3

## Slide 37: Lake-at-rest solutions after 100s (~670 timesteps)
Δx = 1 m
Basis order P = 3

## Slide 38: Steady-state critical flow over uncertain terrain
Flow may transition from subcritical to supercritical
Challenging test with strong nonlinearity, highly non-Gaussian distributions
Nonlinear flow response to linear increase in terrain elevation
Compare stochastic Galerkin results against a Monte Carlo reference solution
Investigate choice of Wiener–Hermite basis order
Measure computational savings

## Slide 39: Linear increase in terrain elevation
Prescribe a hump amplitude a with Gaussian uncertainty with mean 0.6m and stddev 0.3m

## Slide 40: Linear increase in terrain elevation
Prescribe a hump amplitude a with Gaussian uncertainty with mean 0.6m and stddev 0.3m

## Slide 41: Linear increase in terrain elevation
Prescribe a hump amplitude a with Gaussian uncertainty with mean 0.6m and stddev 0.3m

## Slide 42: Linear increase in terrain elevation
Prescribe a hump amplitude a with Gaussian uncertainty with mean 0.6m and stddev 0.3m

## Slide 43: Nonlinear flow response
Upstream boundary
Transmissive water depth
Fixed inflow
Downstream boundary
Fixed water depth
Transmissive outflow
Results of the well-balanced deterministic model, t = 500s
Flow

## Slide 44: Nonlinear flow response
Upstream boundary
Transmissive water depth
Fixed inflow
Downstream boundary
Fixed water depth
Transmissive outflow
Flow

## Slide 45: Nonlinear flow response
Upstream boundary
Transmissive water depth
Fixed inflow
Downstream boundary
Fixed water depth
Transmissive outflow
Flow

## Slide 46: Nonlinear flow response
Upstream boundary
Transmissive water depth
Fixed inflow
Downstream boundary
Fixed water depth
Transmissive outflow
Flow

## Slide 47: Monte Carlo simulation
Results from 2000 iterations of the well-balanced deterministic model

## Slide 48: Stochastic Galerkin simulation
Wiener–Hermite basis order P = 3

## Slide 49: Stochastic Galerkin simulation
Water depth
over hump
Upstream
water depth
Wiener–Hermite basis order P = 3

## Slide 50: Upstream water depth

## Slide 51: Upstream water depth

## Slide 52: Upstream water depth

## Slide 53: Upstream water depth

## Slide 54: Water depth over hump

## Slide 55: Water depth over hump

## Slide 56: Water depth over hump

## Slide 57: Water depth over hump

## Slide 58: Computation time for the steady-state critical flow test
All computation was performed in serial
Stochastic Galerkin P = 3 was ~100 times faster than 2000 Monte Carlo iterations

## Slide 59: Outlook for the Wiener–Hermite basis
Model is theoretically and experimentally well-balanced over uncertain terrain
Accurate flow statistics with low order basis
About 100 times faster than Monte Carlo
High-order bases (P > 3) can produce Gibbs oscillations and non-physical negative water depths
Poor representation of steep gradients in stochastic space

## Slide 60: Wiener–Haar basis
Haar wavelets form a hierarchy of orthogonal basis functions
Basis functions with maximum refinement level 3

## Slide 61: Wiener–Haar basis
Piecewise-constant representation of stochastic space
Maximum refinement level L determines the number of stochastic elements
All operations (addition, pseudo-spectral product, quadrature) are exact
Robust properties are enforced locally over each stochastic element

## Slide 62: Intrusive and non-intrusive approaches with a Wiener–Haar basis
We compare stochastic Galerkin Wiener–Haar model with a non-intrusive sampling approach
The non-intrusive method evaluates the deterministic model at stochastic element midpoints
These are the same points as the stochastic Galerkin quadrature points used to approximate the numerical flux
ξ
Stochastic domain with 8 stochastic elements
(maximum refinement level L = 3)

## Slide 63: Revisiting steady-state critical flow using a Wiener–Haar basis

## Slide 64
Wiener–Hermite
Wiener–Haar

## Slide 65
Wiener–Hermite
Wiener–Haar

## Slide 66
Wiener–Hermite
Wiener–Haar

## Slide 67
Wiener–Hermite
Wiener–Haar

## Slide 68: Extending the stochastic Galerkin model To include wetting-and-drying and uncertain friction
Stochastic Galerkin model is based on a more complex deterministic shallow water discretisation
Extend the Wiener–Haar basis to multiple dimensions

## Slide 69: 2D Wiener–Haar bases
Tensor product basis
1D basis
⊗

## Slide 70: 2D Wiener–Haar bases
Tensor product basis
Truncated basis
Truncation follows Le Maître, Knio, Najm & Ghanem 2004, doi.org/bhsh63

## Slide 71: 2D Wiener–Haar bases
Dynamic wetting-and-drying and friction source term introduces many more nonlinear operations
Majority of operations are approximated by quadrature
Basis truncation does not reduce the number of quadrature points
Hence, little or no computation saving expected using truncated basis

## Slide 72: Revisiting the lake-at-rest
Prescribed uncertainty on topography and initial free-surface elevation using a 2D stochastic domain
Wet and dry zones
Frictionless

## Slide 73: 2D Wiener–Haar tensor product basis

## Slide 74: 2D Wiener–Haar truncated basis

## Slide 75: 2D Wiener–Haar truncated basis

## Slide 76: Simulating a laboratory experiment
Dam break
Triangular obstacle
Frictional bed

## Slide 77: Simulating a laboratory experiment
Prescribed uncertainty over triangular obstacle
Uncertain friction parameter
Uniform distribution

## Slide 78: Stochastic Galerkin solution at t=1.48s
Truncated Wiener–Haar basis leads to negative water depths
Tensor product basis
Truncated basis

## Slide 79: 2D Wiener–Haar tensor product basis

## Slide 80: 2D Wiener–Haar tensor product basis

## Slide 81: 2D Wiener–Haar tensor product basis

## Slide 82: 2D Wiener–Haar tensor product basis

## Slide 83: 2D Wiener–Haar tensor product basis

## Slide 84: 2D Wiener–Haar tensor product basis

## Slide 85: Summary
Wiener–Hermite well-suited for calculating flow statistics in fully-wet domains (river flows)
Wiener–Haar improves representation of probability distributions over Wiener–Hermite
Wiener–Haar tensor product basis inherits all robust properties
Preprint at: bit.ly/wateruq Contact me: js102@zepler.net, @hertzsprrrung

## Slide 86: Summary
Wiener–Hermite well-suited for calculating flow statistics in fully-wet domains (river flows)
Wiener–Haar improves representation of probability distributions over Wiener–Hermite
Wiener–Haar tensor product basis inherits all robust properties
Future directions
How to gain efficiency without sacrificing robustness and stability?
  currently developing a fully-intrusive method with Per
  could wavelet-based adaptivity alleviate the problem?
What are the best alternatives to stochastic Galerkin?
Slides: doi.org/c3nr Preprint: bit.ly/wateruq
Contact: js102@zepler.net, @hertzsprrrung

## Slide 88: Project partners
Industry and government
Academic

## Slide 89: Critical steady-state flow

## Slide 90: Laboratory experiment

## Slide 91: 1D modelling
Source: hecrasmodel.blogspot.com

## Slide 92: 1D-2D coupled modelling
Source: doi.org/fzgc33

## Slide 93: Fully-2D modelling
Source: doi.org/f5h5kb