## Slide 1: Well-balanced stochastic Galerkin shallow flow model with uncertain topography
James Shaw & Georges Kesserwani (University of Sheffield)
Per Pettersson (Norwegian Research Centre)
www.seamlesswave.com

## Slide 2
Measurement errors
Terrain and river bed elevation
River water levels and flow rates
Extrapolation errors
River flow rate often extrapolated from water level
Simulating 1-in-100 year event with only 30–40 years of observation data
Parameter errors
Calibration of friction parameter against observation data
Uncertainties in flood modelling

## Slide 3
Simulation of a 1-in-100 year flood event
20000 Monte Carlo samples
Simulation took 3 days with compute cluster of 100 desktops
Current state-of-the-art
probabilistic flood mapping
Source: Neal et al. 2013 doi.org/c3jj

## Slide 4: Can we do better using a stochastic Galerkin approach?
We seek a stochastic Galerkin model that:
is substantially more efficient than Monte Carlo
produces sufficiently accurate probability distributions
preserves the robust properties of a deterministic model

## Slide 5: Can we do better using a stochastic Galerkin approach?
We seek a stochastic Galerkin model that:
is substantially more efficient than Monte Carlo
produces sufficiently accurate probability distributions
preserves the robust properties of a deterministic model

## Slide 6
Well-balancing: water remains motionless
Robust properties of deterministic models

## Slide 7
Well-balancing: water remains motionless
Dynamic wetting-and-drying (water depth ≥ 0)
Source: hydrologyexpert.com
Robust properties of deterministic models

## Slide 8
Well-balancing: water remains motionless
Dynamic wetting-and-drying
Decades of research into making deterministic models robust
Stochastic Galerkin models do not automatically inherit robustness properties
Robust properties of deterministic models

## Slide 9: Recipe for creating a stochastic Galerkin formulation
Define a basis on the stochastic domain
Define stochastic flow variables as basis expansions
Make a stochastic Galerkin projection of the deterministic formulation onto each basis function
Which basis should we use?
Wiener–Hermite is best for Gaussian distributions
Wiener–Legendre is best for uniform distributions
Wiener–Haar is suitable for arbitrary distributions

## Slide 10: Stochastic Galerkin Wiener–Haar basis
Wiener–Haar basis uses Haar wavelets to provide:
a piecewise-constant approximation
a localised, multiscale representation
direct control over the level of stochastic refinement

## Slide 11: 1D Wiener–Haar basis
1D basis can represent a single source of uncertainty
Refinement level 0
Refinement level 1
Refinement level 2

## Slide 12: 2D Wiener–Haar tensor product basis
⊗
=
2D basis can represent two, joint sources of uncertainty

## Slide 13: Wiener–Haar basis truncation
Following Le Maître et al. 2004, JCP
Tensor product basis
Truncated basis

## Slide 14: Deterministic 1D nonlinear shallow water equations with source terms
Flow vector
Flux vector
Water depth
Discharge (mass flux) per unit width
Terrain slope term
Terrain profile
Friction term
Friction parameter

## Slide 15: Godunov-type finite volume discretisation
Deterministic formulation ensures:
Well-balancing between numerical flux and terrain source term gradients
Non-negative water depths
Numerically stable treatment of frictional forces
Kesserwani 2013, J. Hydraulic Res. Liang and Marche 2009, Adv. Water Res.

## Slide 16: Stochastic Galerkin reformulation
Fixed time step
Flow vectors
Stochastic evolution equation for the kth basis function:
Uniform mesh spacing
Terrain slope term
Roe-approximate Riemann fluxes

## Slide 17: Stochastic Galerkin reformulation
Fixed time step
Flow vectors
Stochastic evolution equation for the kth basis function:
Uniform mesh spacing
Terrain slope source term
Roe-approximate Riemann fluxes
Multiplications (such as q=hu) approximated by pseudo-spectral product
All other nonlinear terms approximated by quadrature
Frictional update applied separately

## Slide 18: Lake-at-rest test case
2D stochastic domain
Prescribed uncertainty on topography and initial free-surface elevation
Wet and dry zones
Frictionless

## Slide 19: 2D Wiener–Haar tensor product basis
Discharge (mass flux) profile after 1000 time steps

## Slide 20: 2D Wiener–Haar truncated basis
Discharge (mass flux) profile after 1000 time steps

## Slide 21: 2D Wiener–Haar truncated basis
Discharge (mass flux) profile after 1000 time steps

## Slide 22: Simulating a laboratory flume experiment
Dam break
Triangular obstacle
Frictional bed

## Slide 23: Simulating a laboratory flume experiment
Uncertainties prescribed to:
Obstacle height
Friction parameter

## Slide 24: 2D Wiener–Haar tensor product basis

## Slide 25: 2D Wiener–Haar tensor product basis

## Slide 26: 2D Wiener–Haar tensor product basis

## Slide 27: 2D Wiener–Haar tensor product basis

## Slide 28: 2D Wiener–Haar tensor product basis

## Slide 29: 2D Wiener–Haar tensor product basis

## Slide 30: 2D Wiener–Haar truncated basis
Model crashes at t = 2.96s. Why?

## Slide 31: 2D Wiener–Haar truncated basis
Basis truncation leads to unphysical negative water depths
Tensor product basis
Truncated basis

## Slide 32: Summary
Wiener–Haar basis facilitates well-balancing, depth positivity preservation
Stochastic Galerkin model preserves robust properties, but only using a tensor product basis
Basis truncation leads to loss of well-balancing and depth positivity
Slides: doi.org/c7mn Preprint: bit.ly/flooduq
Contact: js102@zepler.net, @hertzsprrrung
Future directions
Higher stochastic dimensionality and spatially-correlated topographic errors
Refocus on nonintrusive methods (MLMC, MCMC, sparse grids)
What methods might be most effective?

## Slide 34: Deterministic 1D nonlinear shallow water equations with source terms
z(x) terrain elevation
h(x, t) water depth
u(x, t) depth-average horizontal velocity
q(x, t) discharge (mass flux) per unit width
η(x, t) free-surface elevation

## Slide 35
Quadrature approximation of Roe-approximate Riemann flux:
Pseudo-spectral product approximation of terrain slope term: