## Slide 1: Multi-camera Fourier ptychographic microsocpy
Tomas Aidukas, Pavan C. Konda, Andrew R. Harvey School of Physics and Astronomy,
University of Glasgow
Email: t.aidukas.1@research.gla.ac.uk

## Slide 2: Conventional microscopes are not suitable for high-speed, high-throughput imaging
Conventional microscope
Multi-camera
Fourier ptychography

## Slide 3
Outline
Introduction to multi-camera Fourier ptychography
Experimental design
Computational calibration
Results

## Slide 4
Lens
FT
FT
Synthetic NA
Filtered Spectrum
Diffracted spectrum
Diffracted spectrum
Recorded
image
Recorded image
Tilted illumination
Filtered
spectrum
Filtered
spectrum
Captured spectrum
LED array
Sample
Sensor

## Slide 5
FT
Diffracted spectrum
Filtered
spectrum
Recorded images
Synthetic NA
Captured spectrum
Lens array
LED array
Sample
Sensor array

## Slide 6: Image phase retrieval is required for image stitching
High-resolution estimate
Phase
FT-1
FT
Intensity
Phase
Intensity
Reconstructed image
Repeat for each camera
Spectrum
Spectrum

## Slide 7
Outline
Introduction to multi-camera Fourier ptychography
Experimental design
Computational calibration
Results

## Slide 8: Scheimpflug configuration is used to minimize off-axis aberrations
Scheimpflug intersection
Lens array
Camera array
Sample

## Slide 9: Parallelized image capture reduces image acquisition time up to 9-times
1 camera x 441 LEDs
9 cameras x 49 LEDs

## Slide 10
Outline
Introduction to multi-camera Fourier ptychography
Experimental design
Computational calibration
Results

## Slide 11: Camera and lens array misalignment result in incorrect spectral regions
FT
Correct spectral regions
Recorded images
Estimated spectral region locations

## Slide 12: Camera and lens array misalignment result in incorrect spectral regions
Sensor misalignment
Lens misalignment
Correct spectral regions
Incorrect spectral regions
Recorded images
FT
Estimated spectral region locations

## Slide 13: Errors can be corrected using SURF/SIFT image registration with respect to the central camera
FT
Sensor misalignment
Lens misalignment
Correct spectral regions
Incorrect spectral regions
Recorded images after image registration
Estimated spectral region locations

## Slide 14: Misplaced LED array will shift the spectral regions
LED array misalignment
Actual spectral location
Assumed spectral location
Estimated spectral region locations
Estimated spectral region locations

## Slide 15: Lens array separation errors will shift the spectral regions with respect to the center
Lens array separation errors
LED array misalignment
Actual spectral location
Assumed spectral location
Estimated spectral region locations

## Slide 16: Calibration technique based on spectral analysis can correct for LED and lens array errors
Lens array separation errors
LED array misalignment
Actual spectral location
Assumed spectral location
On-axis illumination
Oblique illumination
Use central camera for LED array corrections
Use off-axis cameras for lens array corrections
Regina Eckert, Zachary F. Phillips, and Laura Waller, "Efficient illumination angle self-calibration in Fourier ptychography," Appl. Opt. 57, 5434-5442 (2018)
Lens array separation errors
LED array misalignment

## Slide 17
Outline
Introduction to multi-camera Fourier ptychography
Experimental design
Computational calibration
Results

## Slide 18
Raw image
Reconstructed image
1 camera x 49 images
Resolution was increased from 8μm to 1.1μm
Image capture time was reduced from 45s to 5s
Reconstructed image
1 camera x 441 images
Reconstructed image
9 cameras x 49 images

## Slide 19
Raw image
Reconstructed image:
9 cameras x 49 images
Reconstructed image:
1 camera x 441 images
Reconstructed phase:
9 cameras x 49 images
-
Radians
SBP was improved from 2-megapixels to 76-megapixels

## Slide 20: Current prototype can capture 1.1um resolution, 76-megapixel images in 5 seconds
For sub-second image capture:
Better hardware → 37FPS vs 12FPS
LED multiplexing → 13 vs 49 images
Brighter LEDs → shorter exposures
Improved design → reduced FOV crop
20