## Slide 1: Sensors in Snowy Alpine Environments: Part II, Sensor Networks with LoRa
James Gallagher
OPeNDAP
<jgallagher@opendap.org>

## Slide 2: Basic Design
Deploy sensors at research sites (initial site: Goat Flat, ~9,000 ft).
Sensor nodes should run on battery power for 2+ years.
Use LoRa radio to connect sensor nodes to a master node.
Use the master node to forward data to the Internet.
The master node will use cell phone technology for Internet uplink.
  Subsequent implementations could use other techniques.
Data from the master node will be sent to an Application Server that can be accessed from browsers and analysis tools.
Locate and Tag sensor nodes using RFID.
The Master node can sense a wide(r) variety of conditions such as snow pack presence.
Calibration: use reference instruments including a portable soil temperature and moisture measurement device.

## Slide 3: Sensor Network: Topology
Master/Sensor star topology
Sensor nodes
  Collect data (temperature, soil moisture, etc.)
  Use LoRa radio to send data to Master
Master
  Receives data from sensors using LoRa
  Forward data to ‘Application Server’ via Internet
Internet
Sensor node
Master node

## Slide 4
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors sleep most of the time to conserve power

## Slide 5
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors wake up and measure environmental parameters

## Slide 6
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors transmit data to the Master

## Slide 7
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors go back to sleep

## Slide 8
Internet
Sensor node
Master node
Sensor Network: Operation
The Master node forwards the collected data to an Application Server in the Internet

## Slide 9
Internet
Sensor node
Master node
Sensor Network: Operation
The Master returns to its nominal mode

## Slide 10: LoRa Network Protocols How the Master and Sensor nodes communicate
LoRaWAN
  Low power requirements
  Reliable transmission; nodes are not responsible for error correction
  Handles security
Ad Hoc protocol*
  Leverage knowledge about the problem to further reduce power used
  Error correction and security must be explicitly coded into the Sensor and Master nodes’ software
  Less flexible than LoRaWAN
Notes: * Often referred to as a ‘datagram protocol,’ however, that’s a misnomer –protocols like LoRaWAN also use datagrams.

## Slide 11: Test Implementation
Sensor node
  LoRa + Arduino + Temperature and soil moisture sensor
  Two LiMnO2 batteries (-50° C)
  Prototypes operated at -25°C and were run buried in both soil and snow as well as in open air
  Total parts cost < $40; options exist to reduce that cost further
Master node
  Dragino
  Combination LoRa/Arduino and Yun single board Linux computer
  Ethernet connectivity to a LAN and then to the Internet
Master/Sensor protocol
  Ad Hoc
Application Server
  CHORDS server running on provisioned Amazon Web Services EC2 instance
  http://soil-sensor-prototype.opendap.org/data

## Slide 12: Sample Data from Second Prototype Running in open air
Prototype was run from 3 to 28 Feb 2019
Sensed air temperature ranged from 0.8° C to -26.75° C

## Slide 13: What is LoRa?
“LoRa (short for long range) is a spread spectrum modulation technique derived from chirp spread spectrum (CSS) technology.”*
Spread Spectrum: To spread an information signal over a (wide) band of radio frequencies.
Robust transmission technique; also used in WiFi, Cell phones, Bluetooth, etc.
Hedy Lamarr and George Antheil are credited with its invention
*https://www.semtech.com/lora/what-is-lora
Antheil2
Lamarr1
Notes: 1 By Unknown - eBay, Public Domain, https://commons.wikimedia.org/w/index.php?curid=47176716
2 By unknown - picture found at http://www.schirmer.com/default.aspx?TabId=2419&State_2872=2&ComposerId_2872=35, Fair use, https://en.wikipedia.org/w/index.php?curid=23450183

## Slide 14: LoRa specifics
Widespread use by Internet of Things applications.
Inexpensive (~$5 eBay; $20 Adafruit/SparkFun)
Small (16mm x 16mm)
Range: 1–10km
Adjustable bit rate: 293 bps to 37.5 kbps
Adjustable error correction, etc., parameters
Works well with Arduino and similar MCUs
Good library support (e.g., RadioHead; TinyLora)
US/EU/AS frequency bands (915/868/430 MHz)
Low power – 20mA receive/100mA transmit
Image from the SparkFun website

## Slide 15: How LoRaWAN Relates to LoRa
Physical layer defined by the radio hardware
Network layer defined by the LoRa Alliance
Physical Layer
Network Layer

## Slide 16: More information
What is LoRa, Semtech website: https://www.semtech.com/lora/what-is-lora
Comparison of LoRa with FSK (frequency Scaled Keying): Jesus Sanchez-Gomez, Ramon Sanchez-Iborra, and Antonio Skarmeta, Transmission Technologies Comparison for IoT Communications in Smart-Cities. 2017. DOI: 10.1109/GLOCOM.2017.8254530.
The Things Network (non-profit) : https://www.thethingsnetwork.org/
MathWorks ThingSpeak: https://thingspeak.com/
LoRa Alliance (non-profit) – LoRaWAN information source: https://lora-alliance.org/
LoRa Datagram open source implementation: https://www.airspayce.com/mikem/arduino/RadioHead/classRHReliableDatagram.html
LoRaWAN open source implementation: https://github.com/adafruit/TinyLoRa

## Slide 17: Extra slides

## Slide 18: Generic IoT/LoRa Topology
Autonomous sensors communicate with LoRa Gateways
LoRa Gateways transfer information to the Internet
Once on the Internet the information can be routed to data servers, etc.
This can use LoRaWAN (a kind of Low Power Wide Area Network – LPWAN) or Datagrams
Picture: Semtech1
Notes: 1https://www.semtech.com/lora/what-is-lora

## Slide 19
Sensor node
Master node
Sensor node
Sensor node
Sensor node
Sensor node
Internet
Internet
Sensor node
Master node