## Slide 1: Combined multi-aperture 3D panoramic thermal imaging and single-photon ranging
Laura V. Cowan1, Ashley Lyons1, Guillem Carles1, James Babington2,3, Andy Wood2, Andrew R. Harvey1
1School of Physics and Astronomy, University of Glasgow, Glasgow, UK G12 8QQ
2Qioptiq Ltd, St Asaph, Denbighshire LL17 0LL, UK
3 now at Thales UK, 1 Linthouse Rd, Glasgow G51 4BZ
Author e-mail address: Andy.Harvey@Glasgow.ac.uk
Notes: Hi, My name is Laura Cowan and I will be talking to you today about my research in combined multi-aperture 3D panoramic thermal imaging and single photon ranging.

## Slide 2
~10m
A
B
Q: How can we provide 3D situational awareness and identification of threats?
Notes: So I'd like to start by presenting a scenario. A solider is walking through unknown territory surrounded by possible threats*. And the question I'd like to ask is* how can we provide 3D situational awareness and identification of threats? So as to know where the threats are? and Are these threats people or not?

## Slide 3
~10m
A
B
Answer:
360 3D Panoramic Imaging
Ranging and imaging occluded objects
Detection of biological micro-movements
What we have done:
Notes: So to answer this question we have created a 360 degree multi-aperture thermal infrared imaging system*. This system has been designed to be integrated into battlefield equipment such as helmets*, but could be used on vehicles or drones also. A threat* such as this solder behind foliage can be identified with thermal imaging and then by introducing a translation*, from point A to B*, stereo vision can be used for passive ranging, and integral imaging can be used to remove* objects occluding the person of interest. Fusing this infrared imaging with single-photon technology* allows for threat detection through precision ranging to detect biological micro-movements such as breathing and material discrimination through impulse response measurement.
Is this threat alive and human or not?

## Slide 4
Notes: Extended applications
Attached to drone
Moving vehicle – reduce risk to life

## Slide 5
The fusion of multi-aperture panoramic thermal imaging and single-photon LIDAR to provide 360° 3D situational awareness and threat detection.

## Slide 6: Presentation Outline
Multi-aperture panoramic imaging
360o 3D situational awareness
  Passive Ranging
  Imaging occluded objects
Fusion with Single Photon LIDAR
  Detection of Breathing
  Material Discrimination
Notes: So what I will present today is the benefits of multi-aperture panoramic imaging. The prototype 360 degree panoramic imaging system and how that allows for 3-dimentional situational awareness providing passive ranging and imaging of occluded objects. I will then discuss the fusion of this technology with single Photon LIDAR for the detection of breathing and material discrimination.

## Slide 7
Compact Panoramic Imaging is not possible using conventional techniques
Trade field-of-view for angular resolution
Total Pixel count limited by detector
Optical aberrations limit resolution
Optical aberrations increase lens complexity, size, weight, cost
[1] Chahl and Srinivasan, Appl Optics (1997).
[2] Pernechele, Opt. Express (2016).
[3] Brady, David J., et al. "Multiscale gigapixel photography." Nature 486.7403 (2012): 386-389.
[1]
[2]
[3]
Notes: Compact panoramic imaging is not possible with conventional imaging techniques.* Traditional approaches consist of using a reflection optic or a hyper hemispherical lens. These approaches limit the total pixel count to that of one detector and the resulting images are highly distorted. *Addressing this through optical design results in an optical system with an increased size, weight, cost, and complexity which is undesirable.

## Slide 8
Curved Detector Array
Curved focal surface reduces optical aberrations and enables simpler optics
Concave Focal surface with single aperture
Convex array of Multiple Cameras
  Panoramic field-of-view of 600 pixels can be achieved
  Scalable to 4 π
[1] Chahl and Srinivasan, Appl Optics (1997)
[1]
MA-TIR Design
Notes: One method of increasing field-of-view while maintaining reduced complexity is with a curved focal surface.* A curved focal surface reduces optical aberrations and enables simpler optics. The reflection optic is replaced with a curved detector array* for example a monocentric single aperture system with a concave focal surface.Or system complexity can be reduced further replacing the central optic with a convex array of low-cost cameras*. This then allows for a scalable architecture. *The design shown here is the schematic of the prototype multi-aperture panoramic thermal infrared system that i will present today.

## Slide 9: Multi-aperture Panoramic Imaging
PHOTO: KEVIN. J. MITCHEL
9 low-cost LWIR FLIR Lepton cameras in convex array
  Each camera 80x60 pixels with short focal length silicon lens
Powered by a low cost single board computer (Raspberry Pi)
Video imaging
PHOTO: KEVIN. J. MITCHEL
Notes: The prototype system comprises 9 low-cost long wave infrared cameras. Each camera has 80 by 60 pixels and a short focal length silicon lens and is powered by a Raspberry Pi. The prototype system can be assembled from off-the shelf components for around 2000 dollars. Which is significantly cheaper than state-of-the-art wide field of view thermal imaging systems. Snapshot and video rate panoramic imaging is possible with this setup.

## Slide 10
link to interactive panoramic video… https://youtu.be/BiIq44osxIo
Panoramic Images and Videos
Snapshot Panoramic Image
Visible Image
0o
360o
180o
Notes: An example of a snapshot panoramic iamge is shown here. Individual images have been stitched together to create a panoramic image covering 360 degrees. The image is much less distorted than that of the reflection optics as shown previously.**This can be shown as a video which has been mapped onto a torus as shown here, to aid image understanding. This can be shown as a virtual reality video.
Displaying panoramic images is well known as being awkward – mapped on to a torus.

## Slide 11
-5
-10
-15
-20
-25
Depth map of People from
Stereo Panoramas
Range (m)
Passive Ranging
[1]
Visible Image
Left Image
Right Image
Left Image
Right Image
Left position
Right position
11
Notes: Passive ranging can be achieved* by translating the system through a scene. *After Recording a panorama at point A and point B.* Areas of interest * can then be segmented in the image, such as people who may pose potential threats* and stereo vision can be used to create a depth map of the scene. In this case the baseline was half a metre where single pixel disparity translates to 40m. This can be extended further for example a footstep equivalent to 1 meter would give a maximum range of

## Slide 12
Passive Ranging
[1]
Left position
Right position
Visible Image
Left Image
Right Image
Left Image
Right Image
-5
-10
-25
-20
-15
Range (m)
Notes: Use of multiple aperture increases versatility
Passive ranging and imaging through obscurants
Two approaches to this – one disparity
Synthetic aperture in time sequence – x10 improvement
Second approach via super resolution image registration
Battlefield Connectivity
Next steps in work plan to take

## Slide 13
Enhanced Situational Awareness - PR

## Slide 14: Imaging through obscurations
Left position
Right position
Elemental Images
Imaging occluded objects with Synthetic Aperture Integral Imaging
0
Refocused on Person
Refocused on Foliage
Depth Map of Person
Depth Map of Foliage
-2
-6
-10
-14
Range (m)
Notes: Further to this integral imaging can be used to image occluded objects. In the scene here there is a person hidden amongst the trees*. When translating the multi-aperture imaging system** the person can be seen through the trees, with a different perspective in each image.* These perspectives can then be registered and summed to refocus on the depth plane of interest.* The objects can then be passively ranged with the stereo vision technique shown previously.

## Slide 15: Single Photon LIDAR
Time correlated single photon counting mode (TCSPC)
Temporal resolution: 300,000 8-bit images per second
Precision Ranging ~1cm
⏄
TRIGGER
SPAD
PULSED
LASER
DIODE
TCSPC Histogram
32x 32 SPAD array
?
Notes: The complementarity of single photon LIDAR is then investigated. *Single photon ranging is acheived in time correlated single photon counting (TCSPC) mode, with an array of single photon avalnche diodes (32 by 32). This system can capture 300,000 8-bit images a second, providing precison ranging on the order of 1cm. This compliments the macro passive ranging achieved with stereo vison, with an accuracy of 0.5m.* This schematic shows our setup for TCSPC mode. *A pulsed laser diode emits light* which hits a beam splitter* directing light to a trigger which starts the clock. Pulsed light then travels towards the scene illuminating the objects of interest.*This is reflected and focussed onto the SPAD array and the clock stops, and a histogram of photon arrival times is produced.
This method is used to interrogate the objects in the scene, what material are they made of and are they breathing or not?

## Slide 16: Detection of biological micromovements
time
Breath out
⏄
TRIGGER
SPAD
PULSED
LASER
DIODE
Are they breathing?
⏄
TRIGGER
SPAD
PULSED
LASER
DIODE
TCSPC Histogram
Breath
out
Breath
in
?
Peak position over time
= yes
Does this oscillate between 0.2 Hz and 0.3 Hz, average adult breathing frequency?
Thermal Image
TCSPC Data Overlaid
= no
Notes: Using the setup from before*, multiple TCSPC histograms are recorded with the aim to determine whether an object is breathing or not. *For example This is a histogram recorded at time A and then this is the histogram recorded half a second later*, they are offset* as they represent a breath in and a breath out. 50 TCSPC histograms are recorded in 3 seconds A gaussian is fitted and the centroid position is extracted and plotted for each histogram** The frequency of the oscillation of the peak centroid position is then categorised as breathing or not breathing.

## Slide 17: Detection of biological micromovements
Where is the person?
Are they breathing?
TCSPC HISTOGRAM
= yes
Average adult breathing frequency
between 0.2 Hz and 0.3 Hz
Visible Image
Thermal Image
TCSPC Data
Overlaid
= no
Position 1
Position 2
Peak position over time

## Slide 18: Material discrimination from Impulse Response
Polystyrene
Aluminium
Flesh
Not Flesh
TCSPC Histograms
α
σ
AL
Polystyrene
Flesh
clothes
α
σ = Width
α = Skewness
Hardness of surface?
Human?
?
Aluminium vs Polystyrene
Flesh vs T-shirt
Plot α vs σ
Notes: Further to this material can be catagorized by measuring the impulse response through TCSPC. * So again is the threat a human or a robot? Polystyrene and Aluminium have been examined to investigate the 'hardness' of a surface. Along with flesh and clothes over flesh to compare the impulse response in each case.* As before the same setup is used to measure TCSPC histograms, and then this distribution is modelled as an exgaussian distribution* where sigma is related to the width of the distribution and alpha is the skewness.* We then plot alpha against sigma and expect the relationship to be warped differently depending on which material is present. * The results are shown here where the relationship is distinct for each material.

## Slide 19: Review and Conclusion
Scalable Multi-aperture panoramic imaging
  3D panoramic imaging for Passive Ranging
  Imaging through obscurations
Fusion with single-photon LIDAR
  Early Threat detection
    Identification of signs-of-life
    Material Discrimination
PHOTO: KEVIN. J. MITCHEL
Refocused on Person
0o
360o
180o
Breathing?
Notes: So to conclude a scalable multi aperture panoramic imaging system has been developed which provides enhanced situational awareness through 3D panoramic imaging capabilities, passive ranging and imaging occluded objects. The fusion with single photon LIDAR has then been explored with the complimentary precision ranging enabling early thread detection through identification of signs of life, such as breathing and material discrimination.

## Slide 20
Thank you for your attention
Please email: Laura.Cowan@glasgow.ac.uk
Interactive 360o Panorama
Notes: Thank you for your attention.