## Slide 1: Combined Optical Raytrace and Monte-Carlo Simulation of Complex Biological Imaging
Guillem Carles and Andrew R. Harvey
School of Physics and Astronomy
University of Glasgow

## Slide 2: Outline
Motivation: modelling of biological imaging
Modelling of Scanning Laser Ophthalmoscope
  Simulation of image formation
  Confocality
  Oximetry
Modelling of Light-Sheet Microscopy
  Diffraction and weak scattering
  Fluorescence
Conclusions

## Slide 3: Motivation
  Biological and Biomedical imaging are extremely active scientific fields that rely on light propagation in turbid media, in particular biological tissue.
Fluorescence [Kerlopian 2008]
Multi-photon microscopy [Kerlopian 2008]
SPIM Microscopy [Ntziachristos 2010]

## Slide 4: Motivation
Scattering of light prevents high-contrast deep-tissue imaging. Range of techniques to circumvent this
Development requires accurate simulation of the system
    1: Light diffusion (sample)
    2: Optical performance (instrument)
[Duke.edu]
[Duke.edu]
[Wikipedia]
[Wikipedia]
[Nat Neuroscience 2001]

## Slide 5: Motivation
1: Light diffusion within turbid media
  Monte-Carlo is the gold standard technique
  Underpins simulation in biological imaging
  Arbitrary system complexity (in principle)
  But, not friendly to the non-expert
2: Optical performance of instrument
  Optical ray-trace software
    Powerful and user friendly
      Zemax-OpticStudio
      OSLO
      Code V
      …

## Slide 6: Motivation
Two components treated in isolation
  Light diffusion in the sample
  Performance of the instrument
Light is not propagated from source to detector
  Rigorous modelling of all components
  Polarisation, fluorescence, coherence, etc.
Connection?
Interaction!

## Slide 7: Motivation
The physical principles of optical ray-trace and Monte-Carlo simulation are the same
Holistic modelling: their integration to simulate the complete imaging process (instrument and sample)
For example:
Notes: (rigorous optical prescriptions, complexity, scattering fluorescence, polarisation)
Aberrations, scattering, chromaticity, etc

## Slide 8: Motivation
Report two examples:
Scanning Laser Ophthalmoscope
Light-Sheet Microscope

## Slide 9: Modelling of SLO

## Slide 10: Modelling of SLO: oximetry
λ=532nm
λ=633nm

## Slide 11: Modelling of SLO: confocality
Pinhole
Less confocal
More confocal
retina
Double pass
Single pass
Confocality increases contrast but reduces SNR

## Slide 12: Modelling of SLO: confocality
Confocality increases contrast but reduces SNR

## Slide 13: Modelling LSFM
Aims, to model:
Realistic optics
Diffraction
Scattering
Fluorescence
DLL: calculate Angular Spectrum

## Slide 14: Conclusions
Reported usage of commercial optical raytracing to perform Monte-Carlo simulation of photon transport
Enables optically-complete simulations of systems
  Complex geometries (through GUI)
  Couple sample/medium and instrument
Benefits
  Construction of rigorous forward-imaging models for inversion
  Investigation of complex setups (rapid virtual prototyping)
  Optimisation of complex systems
  Development/assessment of new computational techniques
  Generation of ground-truth data for training of data-starved algorithms

## Slide 15: Conclusions
Reported examples that illustrate the potential of this approach
Software plugins for rapid and user-friendly virtual prototyping:
    Polarisation-sensitive Mie scattering DLL, with fluorescence
    Angular Spectrum calculator DLL, enables beam diffraction
    Source from database DLL, enables generation of fluorescence
Software available:
  https://github.com/gcarles
  Guillem.CarlesSantacana@glasgow.ac.uk

## Slide 16: Thanks for your attention Guillem.CarlesSantacana@glasgow.ac.uk
Postdoc and PhD positions available in Glasgow in computational microscopy and computational imaging:
contact andy.harvey@glasgow.ac.uk

## Slide 17: Monte Carlo modelling of scattering
Macroscopically; beam extinction due to
Incoming beam
Scattered light
I0
  Scattering
  Absorption
Turbid media
Output Beam
I0
exp(-sz)
exp(-az)
Fluorescence

## Slide 18: Monte Carlo modelling of scattering
One scattering event
ray
Decide distance that ray will travel before it scatters
(probability exp(-sz) to reproduce scattering extinction)
Decide new direction of propagation
(probability defined by the Phase Function)
…and decide new propagation distance again.
This will reproduce macroscopic results after we trace enough rays

## Slide 19: Monte Carlo modelling of scattering
One scattering event: directions and polarisation
General:
Mie scattering:
Phase function:
[van de Hulst, Light scattering by small particles]

## Slide 20: Monte Carlo modelling of scattering
The phase function for Mie scattering

## Slide 21: Monte Carlo modelling of scattering
Tracking electric field enables simulation of coherence phenomena
  E.g. backscattered speckle pattern
Scattering
medium
Incident beam
Detector
Backscattered ray

## Slide 22: Monte Carlo modelling of scattering
Mueller matrices from backscattering (validation)
Incident
Backscattered
Sb = M Si
Stokes vector (1x4)
Polarisation:
Mueller matrix (4x4)

## Slide 23: Monte Carlo modelling of scattering
We coded a DLL that computes all of this within Zemax-OpticStudio

## Slide 24: Monte-Carlo modelling with Zemax
Toy example demonstrating polarisation

## Slide 25: CAD retinal vasculature network
Scanning Laser Ophthalmoscope
[Fundus Image Database (Erlangen-Nuremberg / Brno)]